## Slide 1: Drawings

## Slide 2: What are drawings?
Complete documentation of a design
  Configuration
  Dimensions
  Tolerances
  Bill of Material
  Processing Requirements
  Uniquely Identified
An official, legal document
  Basis of Certification
  Contractual Obligation

## Slide 3: Drawing Numbers vs Part Numbers
Drawing Number uniquely identifies the drawing (a document)
Part Number uniquely identifies the part
Drawing can define single part or assembly of parts
  If single part, Part Number = Drawing Number (sometimes)
  If assembly of parts, Part Number = Drawing Number + Dash Number
Numbering schemes specific to organizations
  Embry-Riddle Example: ME429-F21-01-CLN-01-100
Course
Term
Section
Team ID
Dwg No.
Dash No.
Drawing Number

## Slide 4: Drawing Tree – Water Rocket Launcher
Drawing Tree
Identifies each drawing and part
Defines hierarchy and structure
Defines numbering scheme
EGR201-F20-01-00-1
Water Rocket Launcher
EGR201-F20-01-00-2
Clamp Subassembly
EGR201-F20-01-00-3
Rail Subassembly
EGR201-F20-01-00-4
Base Subassembly
-200 Clamp Subassembly
-201 Tee
-202 Swing Arm
-203 Link, Left
-204 Link, Right
-205 Clip
-210 Plug Subassembly
-300 Rail Subassembly
-301 Rail
-302 Base
-303 Gusset
-400 Base Subassembly
-401 Bottom Plate
-402 Upright, Left
-403 Upright, Right

## Slide 5: Sheet Formats
Drawing Number
Same on each sheet
Short descriptive title
Same on each sheet
Revision
Initial version = “N/C”
Revisions are “A”, “B”, …
Sheet Number
Include number of sheets
Tolerance Block
Avoids tolerancing every dimension
First sheet only
Sheet Size
A = 8.5 x 11
B = 11 x 17
C= 17 x 22 etc.
Material
Only if single part
For assemblies, leave blank and define materials in BOM
First sheet only
Approvals
First sheet only
Proprietary Statement
All sheets
Zone Identifiers
Scale
Label view if different scale

## Slide 6: Assembly Drawings
Follow the drawing tree
One assembly per drawing
  May include subassemblies of a common top assembly
Top assembly assigned its own part number – drawing#-dash# (e.g., EGR201-F20-01-AG-2-200)
First views define the assembly
  Label primary view with assembly dash number and title
  Define only the assembly, not the component parts/subassemblies
    Unless the component feature is created during assembly
  Identify components with balloons corresponding to BOM items
  Show only dimensions created at assembly
    Do not dimension component parts
  Show how the assembly is put together (e.g., weld symbols, fasteners)

## Slide 7
Subsequent views define component parts
  Subassemblies defined on separate drawings and referenced on BOM with complete part number
  Standard hardware and purchased items defined on the BOM (do not draw them)
  Material stock defined on BOM
  Label primary view with part number and title
  Fully dimension and tolerance all manufactured features
    Indicate stock dimensions (e.g., plate thickness) with “STK”

## Slide 8: Example – Water Rocket Launcher
Balloons identify each part/subassembly
Only to level defined on this drawing
Not necessary to call out each instance
Label primary view(s) of top assembly.
Dash number and description
Item No.
Corresponds with balloons.
Part Number
List top assembly first.
Only the Dash Number if defined on this drawing
Complete Part Number if defined elsewhere
Description
Match description on drawing

## Slide 9
Balloons identify each part/subassembly
Label primary view(s) of top assembly.
Dash number and description
Item No.
Corresponds with balloons.
Part Number
List top assembly first.
Dash Number only if defined on this drawing
Complete Part Number if defined elsewhere
Description
Match description on drawing
Material
Be complete – alloy, specification, temper
Better example: 6061-T6 per AMS 4025
Specification sometimes its own column
Stock
Material size as-purchased
No dimensions unless created at assembly

## Slide 10
Label primary view(s) of top assembly.
Dash number and description
Define component parts on subsequent sheets.
No dimensions on isometric views
Fully dimension part. GD&T preferred.

## Slide 11: Drawing Notes
“The use of manufacturing and assembly notes on assembly, subassembly, and detail drawings should be avoided whenever possible.” (Yeah, right.)
List all notes together, preferably on first sheet
Number notes sequentially (do not reuse deleted numbers)
Use separate note for unrelated requirements
Be clear, concise, and grammatically correct
Be as specific as possible without over-constraining
Reference processing specifications, etc. precisely
Do not include contractual items (e.g., cost, payment terms)
Avoid “local notes,” use “flag notes” instead

## Slide 12: Flag Notes
Apply requirement/relief or clarification for a specific drawing feature
Identified by a shaped border (typically a triangle) around the number of the note.
Matching number with border attached to affected drawing feature