## Slide 1: Electrolysis and Material Storage of Hydrogen Gas
Notes: Dylan
Welcome and thank you for coming to embry-riddle hydrogens design concept review. Our project focuses on hydrogen technology, specifically electrolysis and material storage of hydrogen

## Slide 2: Team Members
Hannah Spiller
Lead Material Storage Engineer
Tesla Alford III
Lead Extraction Engineer
Dylan Astrup
Detail Team Lead
Grant Carrabine
Lead Electrolysis Engineer
Jacob Wolf
Lead Piping Engineer
Titan Berson
Lead Interface Engineer
Notes: Dylan

## Slide 3: Agenda
Problem
Solution
Subsystems
Budget
Timeline
Conclusion
Notes: Dylan

## Slide 4: What Embry-Riddle Has
Robotics Lab
Wind Tunnel
Propulsion Lab
Notes: Jacob
Nancy and tracy doryland wind tunnel

## Slide 5: Embry-Riddle Needs Hydrogen Energy Demonstrators
Develop Energy Labs
Create Interest in the Energy Track
Viewable Demonstrations for Visitors
Notes: Jacob

## Slide 6: Generate and Store Hydrogen
ERH2’s purpose is to create an energy demonstrator to generate and store hydrogen.
Embry-Riddle’s Fuel Cell
Notes: Dylan – our purpose is… in order to create facilities to take advantage of the DOE funding

## Slide 7: Hydrogen Storage Applications
Personal Vehicles (Toyota Mirai)
Commercial Vehicles (Toyota)
Aircraft (Airbus)
Storing hydrogen at high pressures and cryogenic temperatures is dangerous and heavy

## Slide 8: System Requirements
Produce Hydrogen
1.1.1 The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.
Store Hydrogen
1.2 The storage method must run the fuel cell for a minimum of 5 minutes
1.2.1 The system must measure the amount of hydrogen stored.
Run Fuel Cell
1.4 The system must interface with the Embry-Riddle fuel cell.
1.4.1 The system output must be a ¼” PTFE tube.
1.1.2 The system must be able to determine the rate of hydrogen gas produced.
Energy Demonstrator
1.3 The system must fit into a 45”x25” box.
Notes: Hannah- don’t read all of this

## Slide 9: ERH2 Proposed System
Electrolyzer
Pressure Gauge
Storage & Extraction
Yor-lock valves
PTFE Tubing
Stainless Steel Pipe
Notes: Jacob
Include fuel cell

## Slide 10: Process Flow Diagram
Simplified PFD
Notes: Jacob
Highlight:

## Slide 11: The ERH2 System
42”
6”
Requirement 1.3
“The system must fit into a 45”x25” box.”
Standard utility cart, 45”x25” top shelf
Notes: Tesla

## Slide 12: Concept of Operations
Weigh material storage capsule
Turn on electrolysis and flush pipe until light turns on
Close exit valve to begin loading material storage
Run electrolysis until pressure gauge reads maximum pressure
Load material storage capsule into pipe using loading rod
Attach yor-lock valve onto pipe
Notes: Dylan

## Slide 13: Concept of Operations
Once at 300C, slowly open exit valve to power fuel cell
Reinsert capsule into pipe using loading rod
Turn on electrolysis and flush pipe until light turns on
Let fuel cell light turn off, close both valves and turn on heating element
Turn off electrolysis, disconnect pipe from valve, remove and weigh the capsule
Notes: Dylan

## Slide 14: Concept of Operations
Step 1: Weigh the material storage capsule using scale and record mass.
Notes: Titan

## Slide 15: Concept of Operations
Step 2: Insert the material storage capsule using a loading rod to ensure the capsule is in the heating zone.
Loading Rod
Notes: Titan

## Slide 16: Concept of Operations
Step 3: Attach stainless steel pipe to Yor-lock valve until wrench tight.
Notes: Titan

## Slide 17: Concept of Operations
Step 4: Ensure all valves are open, turn on the electrolysis machine, and run until the fuel cell light comes on.
Hydrogen Flow
Notes: Titan

## Slide 18: Concept of Operations
Step 5: Continue running electrolysis and close the valve connecting the material storage to the fuel cell.
Hydrogen Flow

## Slide 19: Concept of Operations
Step 6: Continue to run electrolysis until the pressure reaches maximum.
Hydrogen Flow
Maximum: 4 in-WC
Notes: Run tests to figure out absorption curve
Come up with better metric to stop electrolysis

## Slide 20: Concept of Operations
Step 7: Turn off electrolysis, disconnect pipe from valve in a ventilated area, and remove capsule to weigh again.

## Slide 21: Concept of Operations
Step 8: Re-insert capsule by repeating step 2.
Loading Rod

## Slide 22: Concept of Operations
Step 9: Repeat step 4 and then turn off electrolysis.
Hydrogen Flow

## Slide 23: Concept of Operations
Step 10: Once fuel cell light turns off, close both valves, and turn on the heating element.
Hydrogen Flow
Notes: Mention heat to 300C

## Slide 24: Concept of Operations
Step 11: Once the thermocouple reaches 300 degrees Celsius, slowly open the valve to the fuel cell and start timer to measure how long the fuel cell light stays on.
300°C
Notes: Titan

## Slide 25: Electrolysis
Notes: grant

## Slide 26: Electrolysis Overview
1.1.1 Will produce hydrogen
3.1 Will be able to be dissembled
3.2 Hydrogen and oxygen will not mix
3.3 Components are hydrogen resistant
3.4 Amperage must be controlled

## Slide 27: ERH2’s Electrolysis System
Polycarbonate Divider
Hydrogen
Nickel Mesh and Copper Bus
Model of ERH2’s planned Electrolyzer
Oxygen
Requirement 3.1
“The system must be able to be dissembled and reassembled to replace parts.”
Requirement 3.3
“The machine components must not be embrittled by hydrogen.”
Rubber gasket
Bolt
Notes: Grant
21.76 cubic in

## Slide 28: Electrolysis Exploded View
Rubber Gasket
Polycarbonate Spacer
Copper Bus
Threaded Inlet Polycarbonate End Cap
Nickle Mesh
Notes: More explanation
Describe polycarbonate layers

## Slide 29: Alkaline Water
Made from Potassium hydroxide (KOH)
Our system will use a solution of 32%
Typical solution is 32% to 50% in strength [6]
320g KOH into 1 Liter of water

## Slide 30: Alkaline Water Electrolysis

## Slide 31: Mesh Section-View
Hydrogen
Requirement 3.2
“The hydrogen and oxygen produced in the electrolysis system must not mix.”
Oxygen

## Slide 32: Power Requirements
0-20 Amps
Will be able to vary based on production wanted
Minimum 1.23 V [7]
Requirement 3.4
“The amperage going into the system must be controlled and limited to 22.89 amps.”
Notes: https://water.lsbu.ac.uk/water/electrolysis.html#:~:text=The%20minimum%20necessary%20cell%20voltage,is%20the%20potential%201.229%20V.

## Slide 33: Estimate of Hydrogen Needed
Notes: Grant
Calcs on what is need to run the fuel cell at 1 w for 10 minutes
We use National renewable energy laboratory

## Slide 34: Faraday’s Law of Electrolysis Rate of H2 Production
Requirement 1.1.1
“The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.”
Production Consumption
Notes: Grant

## Slide 35: Electrolysis Verification
1.1.1 Will produce hydrogen
3.1 Will be able to be disassembled
3.2 Hydrogen and oxygen will not mix
Alkaline electrolizer will produce hydrogen
Bolts are threaded and reusable gasket
The stalactite layer is used
3.3 Components are hydrogen resistant
Hydrogen embrittlement resistant
3.4 Amperage must be controlled
Control knob on power supply

## Slide 36: Material Storage
Notes: Hannah

## Slide 37: Material Storage Overview
4.2 The storage material must be fully contained within the system.
4.3 The storage material must be at the end of the hydrogen flow.
4.4 The storage material must have a minimum hydrogen density of 2%wt.
1.2 The storage method must run the fuel cell for a minimum of 5 minutes
Notes: Don’t read

## Slide 38: Lithium-Doped Graphitic Carbon Nitride []
Molecular Level
300°C will break the bonds to allow the hydrogen to escape.
=> Carbon Ring
Nitrogen Covalent Bonds
Graphitic Carbon Nitride
Lithium Atoms
Hydrogen Atoms
Notes: This is because the porous structures allow the hydrogen into interior of the nanotubes and pore edges containing double bonded nitrogen provide the active sites for adsorption of hydrogen either physically or chemically.

## Slide 39: Material Capacity
“…it was found that the gravimetric and volumetric densities of hydrogen in both and were greater than 10 wt% and 100 g/L respectively” [1].
Requirement 4.4
“Material must store hydrogen with at least 2% weight of hydrogen gas.”
At 2% wt Hydrogen, the material will store 0.02 grams of hydrogen the amount needed to run the fuel cell for a maximum of 10 minutes.
Needed: 1 g
Requirement 1.2
“The material storage must run the fuel cell for a minimum of 5 minutes.”
Notes: Estimated amount of hydrogen needed

## Slide 40: Material Storage Benefits
 | Compressed Storage | Material Storage
Energy Density | 592.9-3796 J/m^3 | 140-280 J/m^3
Weight Percentage | 3.53% | 2-10%
Storage Pressure | 60-500 bar | 1 bar

## Slide 41: Material Integration
Requirement 4.2
“The storage material must be fully contained within the system.”
Requirement 4.3
“The storage material must be at the end of the hydrogen flow.”
H9 (+25µm)
E9 (-22µm to –75 µm) clearance fit between capsule and pipe
1 Micron Mesh
Hydrogen Flow
Notes: Tesla

## Slide 42: Material Storage Verification
1.2 The storage method must run the fuel cell for a minimum of 5 minutes.
4.2 The storage material must be fully contained within the system.
Material will store at least 0.02 grams of hydrogen, which will run the fuel cell for at least 5 minutes.
The material is in a sealed capsule using a 1-micron mesh press fit.
4.3 The storage material must be at the end of the hydrogen flow.
Material area closed by valves to restrict flow
4.4 The storage material must have a minimum hydrogen density of 2%wt.
Material has a potential capacity of 10%wt.

## Slide 43: Piping
Notes: Jacob

## Slide 44: Piping Overview
5.2 The system must withstand temperatures up to 350°C.
5.3 The temperature at the valves must not exceed 50°C.

## Slide 45: Heat Transfer: Piping’s Purpose
350°C
50°C
50°C
[4]
Requirement 5.2
“The system must withstand temperatures up to 350°C.”
To keep the valves below 50°C, what is the pipe’s required length?

## Slide 46: Determining Heat Transfer Model
Where:
= Energy per unit length, (J/m)
= Density, (kg/m3)
= Cross-sectional area, (m2)
= Specific heat, (J/kg*K)
= Temperature change = 300°C
350°C
50°C
Steel pipe vs. hydrogen gas:
How much energy will each material release over a 350°C to 50°C temperature drop?

## Slide 47: Steel Dominates Thermally
Steel Pipe
= 7,500
=
= 468
= 300
= 53,410
Hydrogen Gas
= 0.076
= 2.3
= 14,500
= 300
= 77
Steel/hydrogen energy ratio:
Thermal energy in hydrogen is negligible compared to thermal energy in steel.
Valve temperature depends primarily on the pipe temperature.

## Slide 48: How to Model the Pipe? Like an Adiabatic Tipped Fin!
350°C
50°C
Heat transfer is due primarily to convection between the pipe and air.
20°C
Treat the system as a fin with an adiabatic tip.
20°C
Notes: No rhetorical question

## Slide 49: Equations for Adiabatic-Tipped Fins
Where:
= pipe length
= outer diameter
= inner diameter
= tip temperature
= base temperature
= air temperature
= external perimeter
= cross-sectional area
= thermal conductivity of steel
= convection coefficient
:
=350°C
=?
=50°C
=.75”
=.68”
Needed: convection coefficient
[8]

## Slide 50: Worst-Case Scenario: Only Natural Convection
Nusselt Number for isothermal horizontal cylinders experiencing natural convection
Where:
= Nusselt Number
= air thermal conductivity
= Rayleigh Number
= Prandtl Number
= surface temperature
= film temperature
Evaluate at T=350°C and T=50°C, see
which case requires the longest pipe
[8]
Needed: Rayleigh Number
Notes: Don’t ignore radiation
"we ignored radiation to make it a conservative estimate"

## Slide 51: Finding Rayleigh Numbers
Where:
= Prandtl Number
= gravitational acceleration =
= coefficient of volume expansion
= kinematic viscosity
= outer diameter = 0.019 (m)
= bulk temperature = 20°C
[8]
= 350°C
= 0.70
*Air properties evaluated at film temperature:
= 50°C
= 0.73

## Slide 52: Finding Required Length
= 350°C
= 5.4
= 0.037
= 10.4
= 24.7
= 4.9
Minimum length: 6 inches
Constant Values
Equations
= 50°C
= 5.0
= 0.026
= 6.8
= 20.1
= 6.0
Requirement 5.3
“The temperature at the valves must not exceed 50°C.”

## Slide 53: Chosen Design
17 (in)
17 (in)
2 (in)
[4]
304 Stainless Steel Pipe
PTFE Tubing
[4]

## Slide 54: Piping Verification
5.2 The system must withstand temperatures up to 350°C.
5.3 The temperature at the valves must not exceed 50°C.
Steel withstands 815°C
Heat transfer analysis

## Slide 55: Extraction

## Slide 56: Extraction Overview
4.1 Must heat to 300°C and not exceed 350°C

## Slide 57: Extraction System
Heating Zone
Heating Element

## Slide 58: Heating Element – Nichrome Wire
Target Temperature for H2 Release: 300°C
Wire Resistance: 2.1Ω/ft.
2in. Heating zone = 10ft of wire
Heater control and Verification - Power supply
- Thermocouples
Notes: Include the insulating material Dr. Heine was proposing for it to sit on
Also how are we connecting it safely, claw clips?

## Slide 59: Heat Transfer Rates
Constant Values
Equation
= 350°C
= 300°C
[8]

## Slide 60: Heat Loss & Required Power
Power Required (), 10ft. of wire @ 300°C: 12.9W
350°C: 15.42W
Heater Resistance ():
300°C Minimum
Voltage: 16.464V Amperage: 0.784A
350°C Maximum
Voltage: 17.995V Amperage: 0.857A
Notes: R = 21 ohm P = 12.9 or 15.42 P=I^2R I_Low=.784 I_High=.857 V_High=17.995 V_Low=16.464

## Slide 61: Thermal Insulation
Insulation Wrap
Aluminum Silicate Fiber
Thermal Conductivity: .085C [7]
Notes: How thick is insulation
Include heat loss through insulation
Mention that the thermal conductivity is

## Slide 62: Extraction Verification
4.1 Must heat to 300°C and not exceed 350°C
Thermocouple – Adjustable by power supply

## Slide 63: Instrumentation
Notes: Dylan

## Slide 64: Instrumentation Overview
1.1.2 Determine rate of hydrogen production
1.2.1 Measure amount of hydrogen stored
6.1 Instrumentation system must be self-reliant

## Slide 65: Pressure Gauges
Requirement 1.1.2
“The system must be able to determine the rate of hydrogen gas produced.”
0-15 inWC (0-0.541 psi)
±2-1-2% accuracy
0-3.75 inWC: ±0.3 inWC
3.75-11.25 inWC: ±0.15 inWC
11.25-15 inWC: ±0.3 inWC

## Slide 66: Thermocouples
2 thermocouples
Integrated at Electrolysis and PTFE interface
Integrated under insulation in heat zone (high temperature insulated probe)

## Slide 67: Thermocouples
Electrolyzer
Thermocouple wire
To thermocouple reader
Notes: Liquid gasket on places needed

## Slide 68: Governing Equations
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Mass of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)
Requirement 1.1.2
“The system must be able to determine the rate of hydrogen gas produced.”

## Slide 69: Mass Measurement
Chemistry lab scale to measure storage system mass
±0.0001 accuracy, 220 g Max
Storage capsule is about 20 grams
Requirement 1.2.1
“The system must measure the amount of hydrogen stored.”

## Slide 70: Instrumentation Verification
1.1.2 Determine rate of hydrogen production
1.2.1 Measure amount of hydrogen stored
6.1 Instrumentation system must be self-reliant
Verified with the pressure gauges and thermocouples using the Ideal Gas Law
Verified with the chemistry scale
All instrumentation is self-contained (analog pressure gauges, battery powered thermocouple reader, battery powered scale)

## Slide 71: Interfaces
Notes: Titan

## Slide 72: Interfaces - Valves
Notes: Show where we are getting it from

## Slide 73: Interfaces – Tee Fittings
Notes: Show where we are getting it from

## Slide 74: Interfaces – Electrolyzer Fitting
Notes: Show where we are getting it from

## Slide 75: Fuel Cell Integration
Requirement 1.4
“The system must interface with the Embry-Riddle fuel cell.”
Requirement 1.4.1
“The system output must be a ¼” PTFE tube.”
¼” PTFE
Notes: Titan

## Slide 76: Detecting Leaks
ERH2 will follow ASHRAE Bubble Method under Chapter 29.9 Leak Detection in the 2017 edition ASHRAE Handbook.
[2]

## Slide 77: Drawings
Notes: Tesla

## Slide 78: Drawing Tree
ME440-S23-01-ERH2-1
ERH2 System Assy.
ME440-S23-01-ERH2-2 Electrolyzer
ME440-S23-01-ERH2-3 Storage Capsule
-200 Electrolyzer
-201 Walls
-202 Space
-203 Stalactite
-204 Copper Bus
-205 Mesh
-206 Rubber Gasket
-300 Storage Capsule
-301 Capsule Body
-302 Cap
In Review

## Slide 79: ERH2 Assembly

## Slide 80: Electrolyzer Assembly

## Slide 81: Storage Capsule Assembly

## Slide 82: Test Matrix
Test Overview | Brief Description | Success Criteria
Leak test | Apply soap solution to interfaces and run compressed air through system. | The test is successful if no bubbles form
Temperature verification | Turn on nichrome wire and measure temperature at heating zone and pipe outlet. | Ends of the pipe do not exceed 60 C and find temperature/power relation
Electrolysis hydrogen production rate | Run electrolysis at different amperages and record change in pressure to determine amount of hydrogen produced. | Electrolysis produces at least 0.002 grams of hydrogen every minute
Material storage capacity | Load material with hydrogen and weigh before and after. | Final mass of the capsule is at least 0.02 grams heavier than the initial mass
Material storage release ratio | Extract hydrogen from material, time how long it runs fuel cell, and weigh the material after. | Final mass of the capsule is equal to the initial mass of the capsule OR the fuel cell is able to run for at least 5 minutes
Material release rate | Extract hydrogen from material and monitor amount with pressure gauge over time. | Pressure gauge indicates a change in pressure equivalent to 0.02 grams of hydrogen over a 10 minute time period
Notes: Hannah first half
Dylan second half

## Slide 83: Risk Analysis
Notes: Titan

## Slide 84: Budget and Schedule
Notes: Dylan

## Slide 85: Budget
Chart: 
| Electrolysis | Material Storage | Extraction | Interfaces | Piping | Instrumentation
 | 321.01 | 392.66 | 201.29 | 382.3 | 83.37 | 150.06
Total: $1530.69
$230.69 over budget
Bill of Materials
Notes: Dylan

## Slide 86: Schedule
January 2023
February 2023
March 2023
April 2023
May 2023
Delta PDR prep
Drawings and CDR prep
Procurement and Fabrication
Test Plans and TRR prep
Testing
15
24
20
9
3
28
Final Report
15
22
CDR
TRR
Symposium
Notes: Dylan

## Slide 87: References
[1] A. Murali, M. Sakar, S. Priya, R. J. Bensingh, and M. A. Kader, “Graphitic-Carbon Nitride for Hydrogen Storage,” in Nanoscale Graphitic Carbon Nitride, Elsevier, 2022, pp. 487–514. doi: 10.1016/B978-0-12-823034-3.00017-0.
[2] “Fast leakage test,” Unitem Wrocław, 28-Apr-2022. [Online]. Available: https://unitemmachines.com/our-offer/fast-leakage-test/. [Accessed: 08-Dec-2022].
[3] “Remington Industries.” [Online]. Available: https://www.remingtonindustries.com/
[4] “McMaster-Carr.” [Online]. Available: https://www.mcmaster.com/
[5] https://www.scielo.br/j/qn/a/KyQvF9DMHK6ZJXyL5zQNy7N/?lang=en&format=pdf
[6] https://www.gichemicals.ie/Potassium-hydroxide.html#:~:text=Potassium%20Hydroxide%20is%20manufactured%20using,concentrated%20to%2050%25%20using%20evaporation.
[7]“Aluminum silicate fiber felt and board,” Aluminum Silicate Fiber Felt and Board. [Online]. Available: https://www.samaterials.com/ceramic-material/2515-aluminum-silicate-fiber-felt-and-board.html. [Accessed: 21-Feb-2023].
[8] Heat Transfer Textbook

## Slide 88: Questions?

## Slide 89: Click to Add Title

## Slide 90: Additional Slides
Requirements
Generation
  Natural Gas
  Photobiological
  Microbial Biomass conversion
Storage
  Physical
  Material
Equations
Graphic Design
Schedule
Ideal Gas

## Slide 91: Generation - Natural Gas
Methane Resource
Methane is collected from a source (usually from natural gas)
Steam-Methane Reforming
High temperature steam (at 700-1,000 °C) is added to the methane gas
Hydrogen Extraction
Hydrogen gas is extracted from the steam-methane mix from an added catalyst
Notes: The common catalyst used for steam-methane is typically nickel but research has been done showing that the noble metals can also work. This process produces hydrogen gas, carbon monoxide, and a small amount of carbon dioxide. DOE did not specify how much CO2 was produced.

## Slide 92: Generation - Photobiological
Bacteria Strain
Water is Supplied
Bacteria Uses Photosynthesis
Water is Broken Down into its Elemental Form
Hydrogen Gas is Released
Notes: After a complete cycle, the bacteria will need some amount of filtration provided, before adding more water. This filtration will remove all nitrates and acidic biproduct chemicals that was produced during a full cycle. During this process the bacteria will consume a percentage of the hydrogen gas, making the gas production rates and net efficiency of the system low.

## Slide 93: Generation - Microbial Biomass Conversion
Bacteria Strain
Hydrocarbon is Added
Bacteria Uses Fermentation
After Fermentation, the Bacteria Leaves Behind Several Elements
Hydrogen Gas can be Filtered Out.

## Slide 94: Storage – Physical Storage
Compressed
5,000-10,000 PSI
Unique Pressure Vessels
Cryogenic
Liquid H2 at -252.2 °C
Solid H2 at -259.14°C

## Slide 95: Storage – Material Storage
Adsorbtion
Hydrogen is Stuck to the Compound’s Surface
Absorption
Hydrogen is Encased by the Compound

## Slide 96: Equations – Area of Mesh

## Slide 97: Equations – Max Current

## Slide 98: Equations – Rate of O2 Production

## Slide 99: Schedule of Project
Date tracking Gantt ERH2 (version 1).xlsb.xlsx

## Slide 100: Ideal Gas Law
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Amount of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)
Calculations

## Slide 101: Heat Loss / Required Power

## Slide 102: Vessel Pressure
Maximum Vessel Pressure: 40.43psia
  Champagne Bottle: 90psia
  Soda Can: 30psia

## Slide 103: Electrolysis Power Circuit
R1 = R3
Nickel Mesh
R2
Salt Water
Notes: Grant
Grant 1.25 in by resistance of saltwater 2 ohms per meter

## Slide 104: Risk Matrix – Before Mitigation
Notes: Hannah

## Slide 105: Pressure Requirement
Hard Copper Pipe
0.5”OD x 0.05”Wall Thickness x 2.63” Long
Requirement 10.2
“-”
PTFE Tubing
0.31”OD x 0.03” Wall Thickness x 2’ Long
Atmospheric Pressure: 14.7psi absolute
Maximum Internal Pressure: 14.7 + 0.29 = 14.99psi absolute
[3]