## Slide 1: Electrolysis and Material Storage of Hydrogen Gas pt. 2
Notes: Dylan
Welcome and thank you for coming to embry-riddle hydrogens design concept review. Our project focuses on hydrogen technology, specifically electrolysis and material storage of hydrogen

## Slide 2: Team Members
Hannah Spiller
Design Team Lead
Tesla Alford III
Lead Extraction Engineer
Dylan Astrup
Lead Human Factors Engineer
Grant Carrabine
Lead Electrolysis Engineer
Jacob Wolf
Lead Piping Engineer
Titan Berson
Lead Interface Engineer
Notes: Hannah and kinda us
My name is Hannah Spiller, I am the design team lead, and this is my team.

## Slide 3: Agenda
Problem
Solution
Subsystems
Budget
Timeline
Conclusion
Notes: ;SHannah
The agenda of today’s presentation will be… Introductions, introducing the problem, our proposed solution, providing all of our evidence, going over the budget, explaining the timeline, and finally conclusions

## Slide 4: DOE Research into Hydrogen
Amount: $32 million
Notes: Tesla

## Slide 5: What Embry-Riddle Has
Robotics Lab
Wind Tunnel
Propulsion Lab
Notes: Jacob
Nancy and tracy doryland wind tunnel

## Slide 6: Embry-Riddle Needs Hydrogen Energy Demonstrators
Develop Energy Labs
Create Interest in the Energy Track
Viewable Demonstrations for Visitors
Notes: Jacob

## Slide 7: Generate and Store Hydrogen
ERH2’s purpose is to create an energy demonstrator to generate and store hydrogen.
Embry-Riddle’s Fuel Cell
Notes: Dylan – our purpose is… in order to create facilities to take advantage of the DOE funding

## Slide 8: System Requirements
1.1 The system must produce hydrogen gas.
1.1.1 The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.
1.1.2 The system must be able to determine the rate of hydrogen gas produced.
1.2 The storage method must run the fuel cell for a minimum of 5 minutes.
1.2.1 The system must measure the amount of hydrogen stored.
1.3 The system must fit into a 4’x2’ box.
1.4 The system must interface with the Embry-Riddle fuel cell.
1.4.1 The system output must be a ¼” PTFE tube.
Notes: Hannah

## Slide 9: Process Flow Diagram
Simplified PFD
Notes: Jacob
Highlight:

## Slide 10: ERH2 Proposed System

## Slide 11: Concept of Operations
Step 1: Weigh the material storage capsule using scale and record mass.

## Slide 12: Concept of Operations
Step 2: Insert the material storage capsule using measurement rod to ensure the capsule is in the heating zone.

## Slide 13: Concept of Operations
Step 3: Attach copper pipe to yor-lock valve until wrench tight.

## Slide 14: Concept of Operations
Step 4: Ensure all valves are open, turn on the electrolysis machine, and run until the fuel cell light comes on.

## Slide 15: Concept of Operations
Step 5:

## Slide 16: The ERH2 System
3.5’
6.0”
Requirement 1.3
“The system must fit into a 4’x2’ box.”
Notes: Tesla

## Slide 17: Fuel Cell Integration
Requirement 1.4
“The system must interface with the Embry-Riddle fuel cell.”
Requirement 1.4.1
“The system output must be a ¼” PTFE tube.”
¼” PTFE
Notes: Titan

## Slide 18: Benefits of ERH2 System
Alternative Energy Storage
Scalable Production Rate
Sole Source of H2 on Campus

## Slide 19: Electrolysis
Notes: grant

## Slide 20: ERH2’s Electrolysis System
Polycarbonate Divider
Hydrogen
Nickel Mesh and Copper Bus
Model of ERH2’s planned Electrolyzer
Oxygen
Requirement 3.1
“The system must be able to be dissembled and reassembled to replace parts.”
Requirement 3.3
“The machine components must not be embrittled by hydrogen.”
Rubber gasket
Notes: Grant
21.76 cubic in

## Slide 21: Alkaline Water
Made from Potassium hydroxide (KOH)
Typical solution is 32% to 50% in strength [6]
Our system will use a solution of 35%
350g KOH into 1 Liter of water

## Slide 22: Alkaline Water Electrolysis
Cathode:
Anode:
[5]

## Slide 23: Mesh Section-View
Hydrogen
Requirement 3.2
“The hydrogen and oxygen produced in the electrolysis system must not mix.”
Oxygen

## Slide 24: Power Supply
Requirement 3.4
“The amperage going into the system must be controlled and limited to 22.89 amps.”
Notes: https://www.amazon.com/Adjustable-Converter-Switching-Regulated-4-Digital/dp/B09QZ1R84M/ref=sr_1_3?keywords=Lab+Power+Supplies+20+amps&qid=1669946118&s=industrial&sr=1-3&ufe=app_do%3Aamzn1.fos.c3015c4a-46bb-44b9-81a4-dc28e6d374b3

## Slide 25: Estimate of Hydrogen Needed
Notes: Grant
Calcs on what is need to run the fuel cell at 1 w for 10 minutes
We use National renewable energy laboratory

## Slide 26: Faraday’s Law of Electrolysis Rate of H2 Production
Requirement 1.1.1
“The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.”
Notes: Grant

## Slide 27: Material Storage
Notes: Hannah

## Slide 28: Lithium-Doped Graphitic Carbon Nitride [/ ]
Molecular Level
300°C

## Slide 29: Material Capacity
“…it was found that the gravimetric and volumetric densities of hydrogen in both and were greater than 10 wt% and 100 g/L respectively” [1].
Requirement 4.4
“Material must store hydrogen with at least 2% weight of hydrogen gas.”
1 g
Requirement 1.2
“The material storage must run the fuel cell for a minimum of 5 minutes.
Notes: Estimated amount of hydrogen needed

## Slide 30: Material Integration
Requirement 4.2
“The storage material must be fully contained within the system.”
Requirement 4.3
“The storage material must be at the end of the hydrogen flow.”
H9 E9 clearance fit between capsule and pipe
Notes: Tesla

## Slide 31: Interfaces
Notes: Titan

## Slide 32: Interfaces - Valves
Notes: Show where we are getting it from

## Slide 33: Interfaces – Tee Fittings
Notes: Show where we are getting it from

## Slide 34: Interfaces – Tee Fittings Con.
Notes: Show where we are getting it from

## Slide 35: Interfaces – Electrolyzer Fitting
Notes: Show where we are getting it from

## Slide 36: Detecting Leaks
ERH2 will follow ASHRAE Bubble Method under Chapter 29.9 Leak Detection in the 2017 edition ASHRAE Handbook.
Requirement 2.1
“The system must allow for safe extraction of hydrogen gas without risk of major leaks.”
[2]

## Slide 37: Piping
Notes: Jacob

## Slide 38: Adiabatic Fin Tip – Best Heat Transfer Model
Compare stainless steel pipe to hydrogen gas:
How much energy will each material release in a 350°C to 50°C temperature drop, on a per-unit-length basis?
Thermal energy in hydrogen is negligible compared to thermal energy in steel.
Negligible heat transfer at the end of the pipe.
  50°C pipe to 20°C air.
Treat the pipe as a fin with an adiabatic tip.

## Slide 39: Adiabatic Fin Treatment
Known:
P perimeter
k thermal conductivity
Ac cross-sectional area
T temperatures
Unknown:
h convection coefficient
Solve for length L

## Slide 40: Finding Convection in the Worst-Case Scenario: Only Natural Convection

## Slide 41: Calculating Required Length
At the tip:
5.3 (in)
5.3 (in)

## Slide 42: Pressure Requirement
Hard Copper Pipe
0.5”OD x 0.05”Wall Thickness x 2.63” Long
Requirement 10.2
“-”
PTFE Tubing
0.31”OD x 0.03” Wall Thickness x 2’ Long
Atmospheric Pressure: 14.7psi absolute
Maximum Internal Pressure: 14.7 + 0.29 = 14.99psi absolute
[3]

## Slide 43: Extraction

## Slide 44: Heating Element – Nichrome Wire
Target Temperature for H2 Release: 300°C
Wire Resistance: 2.1Ω/ft.
Wire Diameter: 1mm (.04 in)
2in. Heating zone 10ft of wire
Requirement 4.1
“The storage material must be heated to 300 degrees Celsius and not exceed 350 degrees Celsius.”
Applied Power: 12.9W
Notes: Include the insulating material Dr. Heine was proposing for it to sit on
Also how are we connecting it safely, claw clips?

## Slide 45: Thermal Insulation – Ceramic Fiber
Material: Calcium Aluminum Silicate Ceramic Fiber
Temperature Rating: -40°C to 800°C
Heat Flow: .82 Btu @ 426°F
Requirement 4.1
“The storage material must be heated to 300 degrees Celsius and not exceed 350 degrees Celsius.”

## Slide 46: Heat Loss & Required Power
Energy Required, 10ft. of wire @ 300°C: 12.9W
350°C: 15.42W
300°C Minimum
Voltage: 12.0V Amperage: 1.075A
350°C Maximum
Voltage: 12.0V Amperage: 1.285A
Requirement 4.1
“The storage material must be heated to 300 degrees Celsius and not exceed 350 degrees Celsius.”

## Slide 47: User Interface (UI)
Notes: Dylan

## Slide 48: Pressure Gauges
0-15 inWC (0-0.541 psi)
±2-1-2% accuracy
    0-3.75 inWC: ±0.3 inWC
    3.75-11.25 inWC: ±0.15 inWC
    11.25-3.75 inWC: ±0.3 inWC
Requirement 1.1.2
“The system must be able to determine the rate of hydrogen gas produced.”

## Slide 49: Thermocouples
2 thermocouples
Integrated at Electrolysis and PTFE interface
Integrated under Insulation in heat zone (high temperature insulated probe)

## Slide 50: Governing Equations
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Mass of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)
Requirement 1.1.2
“The system must be able to determine the rate of hydrogen gas produced.”

## Slide 51: Mass Measurement
Chemistry lab scale to measure storage system mass
±0.0001 accuracy, 220 g Max
Storage capsule is about 20 grams
Requirement 1.2.1
“The system must measure the amount of hydrogen stored.”

## Slide 52: Budget and Schedule
Notes: Dylan

## Slide 53: Subsystem Risk Analysis
Notes: Hannah

## Slide 54: Budget
Chart: ERH2 Budget
| Electrolysis | Material Storage | Extraction | Interfaces | Piping | Instrumentation
 | 321.01 | 392.66 | 201.29 | 382.3 | 83.37 | 150.06
Total: $1530.69
$230.69 over budget

## Slide 55: Schedule
January 2023
February 2023
March 2023
April 2023
May 2023
Delta PDR prep
Drawings and CDR prep
Procurement and Fabrication
Test Plans and TRR prep
Testing
15
24
20
9
3
28
Final Report
15
17
CDR
TRR
Symposium

## Slide 56: References
[1] A. Murali, M. Sakar, S. Priya, R. J. Bensingh, and M. A. Kader, “Graphitic-Carbon Nitride for Hydrogen Storage,” in Nanoscale Graphitic Carbon Nitride, Elsevier, 2022, pp. 487–514. doi: 10.1016/B978-0-12-823034-3.00017-0.
[2] “Fast leakage test,” Unitem Wrocław, 28-Apr-2022. [Online]. Available: https://unitemmachines.com/our-offer/fast-leakage-test/. [Accessed: 08-Dec-2022].
[3] “Remington Industries.” [Online]. Available: https://www.remingtonindustries.com/
[4] “McMaster-Carr.” [Online]. Available: https://www.mcmaster.com/
[5] https://www.scielo.br/j/qn/a/KyQvF9DMHK6ZJXyL5zQNy7N/?lang=en&format=pdf
[6] https://www.gichemicals.ie/Potassium-hydroxide.html#:~:text=Potassium%20Hydroxide%20is%20manufactured%20using,concentrated%20to%2050%25%20using%20evaporation.

## Slide 57: Questions?

## Slide 58: Click to Add Title

## Slide 59: Additional Slides
Requirements
Generation
  Natural Gas
  Photobiological
  Microbial Biomass conversion
Storage
  Physical
  Material
Equations
Graphic Design
Schedule
Ideal Gas

## Slide 60: Requirements Matrix

## Slide 61: Generation - Natural Gas
Methane Resource
Methane is collected from a source (usually from natural gas)
Steam-Methane Reforming
High temperature steam (at 700-1,000 °C) is added to the methane gas
Hydrogen Extraction
Hydrogen gas is extracted from the steam-methane mix from an added catalyst
Notes: The common catalyst used for steam-methane is typically nickel but research has been done showing that the noble metals can also work. This process produces hydrogen gas, carbon monoxide, and a small amount of carbon dioxide. DOE did not specify how much CO2 was produced.

## Slide 62: Generation - Photobiological
Bacteria Strain
Water is Supplied
Bacteria Uses Photosynthesis
Water is Broken Down into its Elemental Form
Hydrogen Gas is Released
Notes: After a complete cycle, the bacteria will need some amount of filtration provided, before adding more water. This filtration will remove all nitrates and acidic biproduct chemicals that was produced during a full cycle. During this process the bacteria will consume a percentage of the hydrogen gas, making the gas production rates and net efficiency of the system low.

## Slide 63: Generation - Microbial Biomass Conversion
Bacteria Strain
Hydrocarbon is Added
Bacteria Uses Fermentation
After Fermentation, the Bacteria Leaves Behind Several Elements
Hydrogen Gas can be Filtered Out.

## Slide 64: Storage – Physical Storage
Compressed
5,000-10,000 PSI
Unique Pressure Vessels
Cryogenic
Liquid H2 at -252.2 °C
Solid H2 at -259.14°C

## Slide 65: Storage – Material Storage
Adsorbtion
Hydrogen is Stuck to the Compound’s Surface
Absorption
Hydrogen is Encased by the Compound

## Slide 66: Equations – Area of Mesh

## Slide 67: Equations – Max Current

## Slide 68: Equations – Rate of O2 Production

## Slide 69: Schedule of Project
Date tracking Gantt ERH2 (version 1).xlsb.xlsx

## Slide 70: Misc. Interfacing Table

## Slide 71: Ideal Gas Law
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Amount of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)
Calculations

## Slide 72: Heat Loss / Required Power

## Slide 73: Vessel Pressure
Maximum Vessel Pressure: 40.43psia
  Champagne Bottle: 90psia
  Soda Can: 30psia

## Slide 74: Electrolysis Power Circuit
R1 = R3
Nickel Mesh
R2
Salt Water
Notes: Grant
Grant 1.25 in by resistance of saltwater 2 ohms per meter

## Slide 75: Risk Matrix – Before Mitigation
Notes: Hannah

## Slide 76: Infographic
Hydrogen Economy Infographic – Herbert Smith Freehills
Requirement 11.3
“The IUI must have an infographic detailing the hydrogen production methods, storage methods, and uses.”