## Slide 1: Electrolysis and Material Storage of Hydrogen Gas
Notes: Hannah
Welcome and thank you for coming to embry-riddle hydrogens design concept review. Our project focuses on hydrogen technology, specifically electrolysis and material storage of hydrogen

## Slide 2: Team Members
Hannah Spiller
Design Team Lead
Tesla Alford III
Dylan Astrup
Grant Carrabine
Jacob Wolf
Titan Berson
Notes: Hannah and kinda us
My name is Hannah Spiller, I am the design team lead, and this is my team.

## Slide 3: Agenda
Introduction
Problem
Solution
Evidence
Budget
Timeline
Conclusion
Notes: ;SHannah
The agenda of today’s presentation will be… Introductions, introducing the problem, our proposed solution, providing all of our evidence, going over the budget, explaining the timeline, and finally conclusions

## Slide 4: Embry-Riddle has a Wind Tunnel
2:00
Notes: Jacob
Nancy and tracy doryland wind tunnel

## Slide 5: Embry-Riddle has a Propulsion Lab
2:00
Notes: Jacob
Test cell three and the propulsion and fabrication test facility

## Slide 6: Embry-Riddle has a Robotics Lab
2:00
Notes: Jacob
Space robotics lab

## Slide 7: Embry-Riddle does not have
Energy Labs
Energy Classrooms
Viewable Demonstrations
3:00
Notes: Jacob

## Slide 8: Energy Research and Interactive Experimentation (EyRIE) Lab
4:00
Notes: Tesla

## Slide 9: DOE Research into Hydrogen
The DOE is researching multiple uses for hydrogen gas, producing the need for more hydrogen. This creates interest within Embry-Riddle to create an EyRIE Lab demonstrator that teaches the general public about hydrogen fuel and storage.
5:00
Notes: Tesla

## Slide 10: Generate and Store Hydrogen
ERH2’s purpose is to create a demonstrator to generate and store hydrogen at ambient conditions.
6:00
Notes: Dylan

## Slide 11: Electrolyzer & Storage
Electrolysis
Material Storage
ERH2’s Electrolyzer
Graphitic Carbon Nitride
7:00
Notes: Grant
Our system will produce and store of hydrogen to demonstrate how hydrogen can be used as an alternative to traditional fuels to generate electricity. This will be done by producing hydrogen to be stored in material-based storage to run the schools fuel cell for 10 minutes at 1 watt.
Basics of how our system will process from electrolysis to material storage then to the fuel cell

## Slide 12: Fuel Cell
The fuel cell provided by the energy department
7:00
Notes: Grant
Our system will produce and store of hydrogen to demonstrate how hydrogen can be used as an alternative to traditional fuels to generate electricity. This will be done by producing hydrogen to be stored in material-based storage to run the schools fuel cell for 10 minutes at 1 watt.
This is an image of the fuel cell we will be using provided by the energy department we will be using to produce hydrogen from our material strage

## Slide 13: How the Electrolyzer Works
https://ptx-hub.org/water-electrolysis-explained/
7:00
Notes: Grant
process by which electric current is passed through a substance to effect a chemical change

## Slide 14: Electrolyzer Breakdown
Plexiglass
Nickel Mesh
Membrane
Model of ERH2’s planned Electrolyzer
Water
Water
Hydrogen
Oxygen
8:00
Notes: Grant
3.1.1 The internal system components should be visible for educational purposes.
1.1 The system must produce hydrogen gas.
1.1.1 The system must produce 0.02 grams of hydrogen gas to run the fuel cell for 10 minutes at 1 watt.
4.2.1 The system must be movable.
Explane the photo pem cell use about .2 grams of water every 10 minutes

## Slide 15: Storing Hydrogen
Sugar
Graphitic Carbon Nitride
9:00
Notes: Titan

## Slide 16: Releasing Hydrogen
Material Storage:
+300°C
10:00
Notes: Titan

## Slide 17: Graphitic Carbon Nitride
Molecular Level
Naked Eye
11:00
Notes: Titan

## Slide 18: System Layout
Simplified PFD
11:00
Notes: Jacob

## Slide 19: Critical Generation Requirements
Notes: Dylan

## Slide 20: Satisfying Housing Requirements
Unit will be approx. 4in x 6in x 6in (LxWxH)
3.1.1
“The internal system components should be visible for educational purposes.”
4.2.1
“Electrolyzer must be movable.”
13:00
Notes: Dylan

## Slide 21: Satisfying Safety Requirements
2.2
“The system must follow Embry-Riddle Prescott Campus’ safety requirements.”
2.1
“The system must allow for safe extraction of hydrogen gas without risk of major leaks.”
14:00
Notes: Dylan
Produces 0.142 grams of H2 in a secure, airtight casing with proper seals.
The electrolyzer follows the ER-PC safety guide
We have also been

## Slide 22: Satisfying Education Requirements
3.1.2.1
“The system must display the approximate amount of hydrogen gas being produced.”
Example of a gas flowmeter
14:00
Notes: Hannah

## Slide 23: Satisfying Generation Requirements
1.1.1
“The system must produce 0.02 grams of hydrogen gas to run the fuel cell for 10 minutes.”
15:00
Notes: Hannah
4.3 The electrolyzer will produce 0.142 grams of H2 exceeding the 0.02 grams required

## Slide 24: Rate of H2 Production
16:00
Faraday’s Law of Electrolysis
Notes: Hannah

## Slide 25: Fuel Cell Requirements
17:00
Notes: Grant
Calcs on what is need to run the fuel cell at 1 w for 10 minutes

## Slide 26: Generation - Decision Matrix
GENERATION | Weighting | SMR (Datum) | Biological | Electrolysis
Cost | 1 | - | -1 | 1
Production rate | 2 | - | -1 | -1
System efficiency | 3 | - | -1 | 1
Total |  | - | -5 | 2
19:00
Notes: Titan

## Slide 27: Critical Storage Requirements
Notes: Titan

## Slide 28: Satisfying Storage Requirements
1.2
“The system must store 0.04 grams of hydrogen gas.”
20:00
Notes: Tesla

## Slide 29: Satisfying Storage Requirements
2.1
“The system must allow for safe extraction of hydrogen gas without risk of major leaks.”
21:00
Notes: Tesla

## Slide 30: Storage Methods
Storing Hydrogen
Physical Based
Material Based
22:00
Notes: Tesla

## Slide 31: Carbon Nitride is Best for Storage
STORAGE | Weighting | Physical (Datum) | Metal Hydride | Intermetallic Hydride | Chemical Hydride | Carbon Nitride
Cost | 2 | - | 1 | 1 | 1 | 1
Capacity | 3 | - | -1 | -1 | -1 | 1
Discharge rate | 1 | - | -1 | 1 | 1 | -1
Total |  | - | -2 | 0 | 0 | 4
24:00
Notes: Titan

## Slide 32: Budget
INCOME |  | 
 | Base | $1,300.00
 | TOTAL INCOME | $1,300.00
EXPENSES |  | 
 | Electrolysis | $675.00
 | Material Storage | $230.00
 | Charge/Discharge | $87.00
 | Plumbing | $24.00
 | Instrumentation | $400.00
 | Valves | $80.00
 | Sealant | $30.00
 | Electrical | $30.00
 | Team Shirts | $80.00
 | TOTAL EXPENSES | $1,636.00
TOTAL |  | $(336.00)
26:00
Notes: Hannah
Expenses are overestimates

## Slide 33: Schedule
Task | Start Date | End Date
Build Electrolysis | 2/13/2023 | 3/3/2023
Assemble Plumbing | 3/6/2023 | 3/20/2023
Valves and Seals | 3/20/2023 | 3/31/2023
Final Report | 2/15/2023 | 4/28/2023
27:00
Notes: Hannah

## Slide 34: Schedule
28:00
Notes: Hannah

## Slide 35: Acknowledgements
Dr. Karl Heine
Dr. Johnathan Adams
Dr. Richard DiPietro
Dr. Hillary Eaton
Professor Rachel Schmidt
Dr. Istemi Ozsoy
Dr. David Lanning
Dr. Robert Murray-Smith
AXFAB Staff
Mansidak Singh
30:00
Notes: Hannah

## Slide 36: Questions?

## Slide 37: Additional Slides
Requirements
Generation
  Natural Gas
  Photobiological
  Microbial Biomass conversion
Storage
  Physical
  Material
Equations
Graphic Design
Schedule

## Slide 38: Requirements Matrix

## Slide 39: Generation - Natural Gas
Methane Resource
Methane is collected from a source (usually from natural gas)
Steam-Methane Reforming
High temperature steam (at 700-1,000 °C) is added to the methane gas
Hydrogen Extraction
Hydrogen gas is extracted from the steam-methane mix from an added catalyst
Notes: The common catalyst used for steam-methane is typically nickel but research has been done showing that the noble metals can also work. This process produces hydrogen gas, carbon monoxide, and a small amount of carbon dioxide. DOE did not specify how much CO2 was produced.

## Slide 40: Generation - Photobiological
Bacteria Strain
Water is Supplied
Bacteria Uses Photosynthesis
Water is Broken Down into its Elemental Form
Hydrogen Gas is Released
Notes: After a complete cycle, the bacteria will need some amount of filtration provided, before adding more water. This filtration will remove all nitrates and acidic biproduct chemicals that was produced during a full cycle. During this process the bacteria will consume a percentage of the hydrogen gas, making the gas production rates and net efficiency of the system low.

## Slide 41: Generation - Microbial Biomass Conversion
Bacteria Strain
Hydrocarbon is Added
Bacteria Uses Fermentation
After Fermentation, the Bacteria Leaves Behind Several Elements
Hydrogen Gas can be Filtered Out.

## Slide 42: Storage – Physical Storage
Compressed
5,000-10,000 PSI
Unique Pressure Vessels
Cryogenic
Liquid H2 at -252.2 °C
Solid H2 at -259.14°C

## Slide 43: Storage – Material Storage
Adsorbtion
Hydrogen is Stuck to the Compound’s Surface
Absorption
Hydrogen is Encased by the Compound

## Slide 44: Equations – Area of Mesh

## Slide 45: Equations – Max Current

## Slide 46: Equations – Rate of O2 Production

## Slide 47: Schedule of Project
Date tracking Gantt ERH2 (version 1).xlsb.xlsx