## Slide 1: Electrolysis and Material Storage of Hydrogen Gas
Notes: Hannah
Welcome and thank you for coming to embry-riddle hydrogens design concept review. Our project focuses on hydrogen technology, specifically electrolysis and material storage of hydrogen

## Slide 2: Team Members
Hannah Spiller
Design Team Lead
Tesla Alford III
Lead Extraction Engineer
Dylan Astrup
Lead Human Factors Engineer
Grant Carrabine
Lead Electrolysis Engineer
Jacob Wolf
Lead Piping Engineer
Titan Berson
Lead Interface Engineer
Notes: Hannah and kinda us
My name is Hannah Spiller, I am the design team lead, and this is my team.

## Slide 3: Agenda
Introduction
Problem
Solution
Subsystems
Budget
Timeline
Conclusion
Notes: ;SHannah
The agenda of today’s presentation will be… Introductions, introducing the problem, our proposed solution, providing all of our evidence, going over the budget, explaining the timeline, and finally conclusions

## Slide 4: What Embry-Riddle Has
Robotics Lab
Wind Tunnel
Propulsion Lab
Notes: Jacob
Nancy and tracy doryland wind tunnel

## Slide 5: Embry-Riddle does not have
Energy Labs
Energy Classrooms
Viewable Demonstrations
Notes: Jacob

## Slide 6: DOE Research into Hydrogen
  The DOE is researching multiple uses for hydrogen gas, producing the need for more hydrogen. This creates interest within Embry-Riddle to create an alternative energy demonstrator that teaches the general public about hydrogen fuel and storage.
Amount: $32 million
Notes: Tesla

## Slide 7: Generate and Store Hydrogen
ERH2’s purpose is to create a demonstrator to generate and store hydrogen.
Notes: Dylan

## Slide 8: Benefits of ERH2 System
Alternative Energy Storage
Scalable Production Rate
Sole Source of H2 on Campus
Notes: Dylan

## Slide 9: The ERH2 System
Electrolysis
Pressure Gauge
Nichrome Wire
Material Storage
Fuel Cell
Diverting Valve
Notes: Tesla

## Slide 10: Process Flow Diagram
Simplified PFD
Notes: Jacob

## Slide 11: Critical System Requirements
Produce 0.02 grams of hydrogen over 10 minutes
Store 0.04 grams of hydrogen
Safely extract hydrogen from system
Internal components visible
Notes: Hannah

## Slide 12: Electrolysis Equation
Notes: Titan

## Slide 13: Hydrogen Production Requirement
Notes: Grant
Calcs on what is need to run the fuel cell at 1 w for 10 minutes
We use National renewable energy laboratory

## Slide 14: Electrolysis
Notes: grant

## Slide 15: Subsystem Requirements
6.1 The hydrogen and oxygen produced in the electrolysis system must not mix.
6.2 The electrolysis system housing layers must be replaceable.
6.3 The electrolysis system housing must be resealable.
Notes: 21

## Slide 16: Subsystem Requirements
6.4 The electrolysis system housing must not be electrically conductive.
6.5 All wires must be insulated and sized according to the National Electrical Code.
6.6 The amperage applied to the electrolysis system must not exceed 20 amps.
6.7 The electrolysis system must have an emergency kill switch.

## Slide 17: Electrolysis Breakdown
Plexiglass Divider
Hydrogen
Nickel Mesh
Model of ERH2’s planned Electrolyzer
Oxygen
Water reservoir channel below water level for sealing [6.1]
System fastened by bolts for changing layers [6.2]
Rubber tape between layers to seal [6.3]
Notes: Grant
21.76 cubic in

## Slide 18: Mesh Section-View
Plexiglass
Hydrogen
Nickel Mesh
Empty Area will be filled with water

## Slide 19: Power Supply
20-24 Amps
60 Volts
Kill Switch [6.7]
Amperage Control [6.6]
Notes: https://www.amazon.com/Adjustable-Converter-Switching-Regulated-4-Digital/dp/B09QZ1R84M/ref=sr_1_3?keywords=Lab+Power+Supplies+20+amps&qid=1669946118&s=industrial&sr=1-3&ufe=app_do%3Aamzn1.fos.c3015c4a-46bb-44b9-81a4-dc28e6d374b3

## Slide 20: Faraday’s Law of Electrolysis Rate of H2 Production
Notes: Grant

## Slide 21: Electrolysis Power Circuit
R1 = R3
Nickel Mesh
R2
Salt Water
Notes: Grant 1.25 in by resistance of saltwater 2 ohms per meter

## Slide 22: Electrolysis Summary
Requirement | Design | Expected Performance | Verification
6.1 | The hydrogen and oxygen will be separated at creation | 100% | Fuel Cell Runs
6.2 | The system was designed to be sandwiched together into different layers making it replaceable | Life of bolts used | It will come apart
6.3 | Ability to bolt together | The life span of seals | It will come apart
Notes: Grant

## Slide 23: Electrolysis Summary
Requirement | Design | Expected Performance | Verification
6.4 | Will be made of plastic | Nonconductive | Voltmeter
6.5 | Will use 12-gauge wire | Rated for 20 amp | National Electrical code
6.6 | Will set power supply to max 20 amps | Max 20 amps | Power supply read out
6.7 | Have and on off switch | 100% | System turns off
Notes: Grant

## Slide 24: Material Storage
Notes: Titan

## Slide 25: System Requirements
1.2
“The system must store 0.04 grams of hydrogen gas.”
4.1
“The material storage efficiency (hydrogen in vs. hydrogen out) must be at least 50%.”
Notes: 0.04 is 2x the amount needed for potential losses and must release at least half of the hydrogen going in

## Slide 26: Lithium-Doped Graphitic Carbon Nitride [/ ]
Molecular Level
Naked Eye
Notes: Dope with lithium to get maximum storage capacity, manufacturable on campus, hydrogen is absorbed at ambient conditions,

## Slide 27: Subsystem Definition
The material storage subsystem is made up of a graduated bottle holding graphitic carbon nitride and rubber stopper to seal the bottle.
Material Storage
Graduated Bottle
Rubber Seal
Notes: Hydrogen comes into the 1L bottle and then the storage is heated

## Slide 28: Subsystem Requirements
7.1 Material storage must release 0.02 grams of hydrogen.
7.2 Material must store hydrogen with at least 2% weight of Hydrogen.
7.3 Must contain at least 2 grams of material storage.

## Slide 29: Equations
Where:
= Material Efficiency
= Mass of hydrogen into the material storage system
= Mass of hydrogen leaving the material storage subsystem.
= Mass of hydrogen stored in material storage
= Mass of the storage before hydrogen is introduced
= Final mass of the material after hydrogen loading
= Weight percentage of hydrogen in the material storage

## Slide 30: 7.1 Release
Release Rate Testing
Scalable mass to increase hydrogen being released
Valve to contain hydrogen If slow release
Material Storage
Fuel Cell
Notes: No current data on release rate, DOE funding research, easily scalable or contained

## Slide 31: 7.2 Material Capacity
“…it was found that the gravimetric and volumetric densities of hydrogen in both and were greater than 10 wt% and 100 g/L respectively” [Wu et al.]
Notes: Minimum of 2%

## Slide 32: 7.3 Material Needed
4% yield Urea to Graphitic Carbon Nitride
https://www.homesciencetools.com/product/lithium-chloride-30-g/
https://www.google.com/search?q=urea&rlz=1C1GCEJ_enUS1034&source=lnms&tbm=isch&sa=X&ved=2ahUKEwjL07Cd_dn7AhVxBEQIHctsDisQ_AUoAXoECAEQAw&biw=1920&bih=969#imgrc=uJswUlCxh-9elM
Notes: Pyrolysis of urea

## Slide 33: Storage Summary
Requirement | Design | Expected Performance | Verification
7.1 | Extraction heats material to release temperature | Releases at least 0.02 grams per 10 minutes | Runs the fuel cell
7.2 | Doped graphitic carbon nitride | Capacity of 10% wt hydrogen | Numerically, Greater than 2% Testing
7.3 | 2 grams of Graphitic Carbon Nitride | Synthesize 50 grams for 4% yield | Greater than 2 grams

## Slide 34: System Interfaces

## Slide 35: System Requirements
4.4
“all subsystem interfaces must be sealed.”
Notes: Tesla

## Slide 36: Interface Map
3-Way Diverting Valve, Brass
Barbed Fitting, Stainless
Rubber Stopper
3-Way Barbed Insert, Brass
1 in
1 - 1/16 in
1 - 21/64 in
.4375 in Through Hole
½ in OD Yor-Loks
¼ in OD
¼ in NPT, 18 TPI
¼ in OD

## Slide 37: Detecting Leaks
ERH2 will follow ASHRAE Bubble Method under Chapter 29.9 Leak Detection in the 2017 edition ASHRAE Handbook.
Fast leakage test – Unitem Wrocław (unitemmachines.com)

## Slide 38: Integration Summary
Requirement | Design | Expected Performance | Verification
8.1 | The electrolyzer fitting moves hydrogen gas from the electrolyzer to the piping. | No leaks | Bubble Test
8.2 | The pressure gauge fitting moves hydrogen gas from the piping to the pressure gauge. | No leaks | Bubble Test
8.3 | The rubber stoper fitting moves hydrogen gas from the 3-way diverting valve to the material storage. | No leaks | Bubble Test

## Slide 39: Extraction

## Slide 40: System Requirements
2.1
“The system must allow for safe extraction of hydrogen gas without risk of major leaks.”
4.3
“The material storage to fuel cell system must be able to run for 10 minutes.”
Notes: Tesla

## Slide 41: Subsystem Requirements
9.1 The heating system must be able to cause the material storage to off-gas hydrogen at a rate which yields a gauge pressure less than 2000pa gauge or 0.29psi gauge.
9.2 The heating system must be able to heat the storage material to 300°C and must not exceed 350°C.

## Slide 42: Heating Element – Nichrome Wire
-Remington Industries
Target Temperature: 300°C
Maximum Temperature: 350°C
Thermal Insulation:
Aerogel - 650 °C
Notes: Include the insulating material Dr. Heine was proposing for it to sit on
Also how are we connecting it safely, claw clips?

## Slide 43: Heat Loss Calculations
Energy Loss, 10ft. Of wire @ 300°C: 2.683W
= 2.5 for still air
A1= .0038m2 (50% surface area)
A2= .0019m2 (25% surface area)
K= 11.3
∆𝑇= 280°

## Slide 44: Power Input Calculations
Voltage Requirement: 2.402V Amperage: 1.118A

## Slide 45: Vessel Pressure
PV=nRT
  V = 1.1L T = 300°C R = 287
Maximum Vessel Pressure: 40.43psia
  Champagne Bottle: 90psia
  Soda Can: 30psia

## Slide 46: Extraction Summary
Requirement | Design | Expected Performance | Verification
9.1 | Nichrome wire achieves steady state temperature of 300°C | Hydrogen release from storage medium | Fuel cell produces electricity
9.2 | Voltage supplied to Nichrome wire ≈ 2.4V | Steady state temp. < 350°C | Thermal Camera (Propulsion Lab)

## Slide 47: Piping
Notes: Jacob

## Slide 48: Piping Layout
PTFE Tubing
Copper Piping
Notes: Chose PTFE for transportability
Chose copper for heat transfer

## Slide 49: Subsystem Requirements
10.1 The subsystem must transport hydrogen gas from the electrolyzer to the material storage, and from the material storage to the fuel cell.
10.2 The subsystem must withstand internal pressures up to 0.29psi gauge without leaking.
10.3 The subsystem must withstand temperatures up to 350°C without leaking.

## Slide 50: Heat Transfer Analysis
Use a 6in long pipe at constant 100°C that reduces internal gas temperature from 300°C to 150°C to determine flow regime.
Analyze 0.0001in long sections where pipe is average temperature of internal and external air.

## Slide 51: Piping Requirement Summary
Requirement | Design | Expected Performance | Verification
10.1 | PTFE tubing and copper pipe. | Transportation of hydrogen gas | Pressure gauge, mass of material storage, operation of fuel cell
10.2 | Material chosen to withstand pressures. | No leaks | Bubble method
10.3 | Copper piping sufficiently transfers heat. | Temperature reduced to 50°C at diverting valve | Thermal imaging
Hard Copper Pipe 0.5”OD x 0.05”Wall Thickness x 2.63” Long
PTFE Tubing 0.31”OD x 0.03” Wall Thickness x 2’ Long

## Slide 52: Interactive User Interface (IUI)
Notes: Dylan

## Slide 53: Subsystem Requirements
11.1 states that the system must include a pressure gauge integrated in the hydrogen piping
11.2 states that the system must include a scale to mass the material storage system
11.3 states that the IUI must have an infographic about hydrogen production, storage, and uses
11.4 states that the IUI must display all measured values
11.5 states that the IUI displays must display values in English units

## Slide 54: 11.1 Pressure Gauge
0-30 inWC (0-1.08 psi)
±3-2-3% accuracy
0-7.5 inWC: ±0.9 inWC
7.5-22.5 inWC: ±0.6 inWC
22.5-30 inWC: ±0.9 inWC

## Slide 55: Governing Equations
In. wc | PSI | Grams of Hydrogen
0 | 0 | 0
1 | 0.0360912 | 0.000247124
2 | 0.0721824 | 0.000494249
3 | 0.1082736 | 0.000741373
4 | 0.1443648 | 0.000988497
5 | 0.180456 | 0.001235621
6 | 0.2165472 | 0.001482746
7 | 0.2526384 | 0.00172987
8 | 0.2887296 | 0.001976994
9 | 0.3248208 | 0.002224119
10 | 0.360912 | 0.002471243
11 | 0.3970032 | 0.002718367
12 | 0.4330944 | 0.002965492
13 | 0.4691856 | 0.003212616
14 | 0.5052768 | 0.00345974
15 | 0.541368 | 0.003706864
16 | 0.5774592 | 0.003953989
17 | 0.6135504 | 0.004201113
18 | 0.6496416 | 0.004448237
19 | 0.6857328 | 0.004695362
20 | 0.721824 | 0.004942486
21 | 0.7579152 | 0.00518961
22 | 0.7940064 | 0.005436735
23 | 0.8300976 | 0.005683859
24 | 0.8661888 | 0.005930983
25 | 0.90228 | 0.006178107
26 | 0.9383712 | 0.006425232
27 | 0.9744624 | 0.006672356
28 | 1.0105536 | 0.00691948
29 | 1.0466448 | 0.007166605
30 | 1.082736 | 0.007413729
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Amount of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)

## Slide 56: 11.2 Mass Measurement
Chemistry lab scale to measure storage system mass
±0.0005 accuracy

## Slide 57: 11.3 Infographic
Hydrogen Economy Infographic – Herbert Smith Freehills

## Slide 58: IUI Summary
Requirement | Design | Expected Performance | Verification
11.1 | 0-30 inWC Pressure Gauge | Display accurate pressure of system | Visual Inspection
11.2 | Chemistry lab digital scale | Display mass of hydrogen in storage system | Visual Inspection
11.3 | Hydrogen Economy Infographic | Inform about hydrogen economy | Visual Inspection
11.4 | Pressure gauge and scale have measurement displays | Display measurements | Visual Inspection
11.5 | Pressure gauge and scale have English unit on the displays | English Units | Visual Inspection

## Slide 59: Risk Matrix – Before Mitigation
Notes: Hannah

## Slide 60: Risk Matrix – After Mitigation
Notes: Hannah

## Slide 61: Budget
Item | Cost
Shirts | $150.00
Urea | $20.00
lithium Chloride 30grams | $17.90
Plexiglass | $84.56
Pressure gauge | $35.65
Mesh X 2 | $22.00
PTFE Tubing x 25ft | $62.25
F-F Thread Adapter x2 | $19.12
Bolts | $7.60
Copper Pipe (2ft) | $5.49
Barbed T fitting x 2 | $24.28
Barbed Fitting x3 | 9.02
Graduated Bottle | 91.64
Nichrome Wire 20gauge x 50ft | $12.00
Solder | $30
Rubber Plug | $10.42
Rubber Tape (25ft) | 18.37
Diverting Valve | 123.84
Epoxy's | $30
nuts | $2.20
Other Plastic | $88.04
Power Supply | $289.99
Total | 
$1,154.37 | 
Notes: Hannah
Expenses are overestimates

## Slide 62: Schedule
Notes: Hannah

## Slide 63: Acknowledgements
Dr. Karl Heine
Dr. Johnathan Adams
Dr. Richard DiPietro
Dr. Istemi Ozsoy
Dr. David Lanning
AXFAB Staff
Taylor Spiller
Notes: Hannah

## Slide 64: Questions?

## Slide 65: Additional Slides
Requirements
Generation
  Natural Gas
  Photobiological
  Microbial Biomass conversion
Storage
  Physical
  Material
Equations
Graphic Design
Schedule

## Slide 66: Requirements Matrix

## Slide 67: Generation - Natural Gas
Methane Resource
Methane is collected from a source (usually from natural gas)
Steam-Methane Reforming
High temperature steam (at 700-1,000 °C) is added to the methane gas
Hydrogen Extraction
Hydrogen gas is extracted from the steam-methane mix from an added catalyst
Notes: The common catalyst used for steam-methane is typically nickel but research has been done showing that the noble metals can also work. This process produces hydrogen gas, carbon monoxide, and a small amount of carbon dioxide. DOE did not specify how much CO2 was produced.

## Slide 68: Generation - Photobiological
Bacteria Strain
Water is Supplied
Bacteria Uses Photosynthesis
Water is Broken Down into its Elemental Form
Hydrogen Gas is Released
Notes: After a complete cycle, the bacteria will need some amount of filtration provided, before adding more water. This filtration will remove all nitrates and acidic biproduct chemicals that was produced during a full cycle. During this process the bacteria will consume a percentage of the hydrogen gas, making the gas production rates and net efficiency of the system low.

## Slide 69: Generation - Microbial Biomass Conversion
Bacteria Strain
Hydrocarbon is Added
Bacteria Uses Fermentation
After Fermentation, the Bacteria Leaves Behind Several Elements
Hydrogen Gas can be Filtered Out.

## Slide 70: Storage – Physical Storage
Compressed
5,000-10,000 PSI
Unique Pressure Vessels
Cryogenic
Liquid H2 at -252.2 °C
Solid H2 at -259.14°C

## Slide 71: Storage – Material Storage
Adsorbtion
Hydrogen is Stuck to the Compound’s Surface
Absorption
Hydrogen is Encased by the Compound

## Slide 72: Equations – Area of Mesh

## Slide 73: Equations – Max Current

## Slide 74: Equations – Rate of O2 Production

## Slide 75: Misc. Interfacing Table

## Slide 76: Schedule of Project
Date tracking Gantt ERH2 (version 1).xlsb.xlsx