## Slide 1: Electrolysis and Material Storage of Hydrogen Gas
Notes: Dylan
Welcome and thank you for coming to embry-riddle hydrogens design concept review. Our project focuses on hydrogen technology, specifically electrolysis and material storage of hydrogen

## Slide 2: Team Members
Hannah Spiller
Lead Material Storage Engineer
Tesla Alford III
Lead Extraction Engineer
Dylan Astrup
Detail Team Lead
Grant Carrabine
Lead Electrolysis Engineer
Jacob Wolf
Lead Piping Engineer
Titan Berson
Lead Interface Engineer
Notes: Dylan

## Slide 3: Agenda
Problem
System Requirements
Verification Tests
Conclusion
System Description
Limiting Factors
Future Suggestions
Notes: Dylan

## Slide 4: What Embry-Riddle Has
Robotics Lab
Wind Tunnel
Propulsion Lab
Notes: Jacob
Nancy and tracy doryland wind tunnel

## Slide 5: What Embry-Riddle Needs
Energy Labs
Create Interest in the Energy Track
Viewable Demonstrations
Notes: Jacob

## Slide 6: Hydrogen Storage Applications
Personal Vehicles
Commercial Vehicles
Aircraft
Storing hydrogen at high pressures and cryogenic temperatures is dangerous and heavy.
Notes: Hannah: Using Hydrogen as a fuel is a potential clean energy solution across many applications, including transportation. Toyota is developing personal vehicles and commercial vehicles that use hydrogen as fuel. A potential problem with hydrogen is that it is currently stored at high pressures or cryogenic temperatures. This is extremely heavy and is potentially dangerous.

## Slide 7: Generate and Store Hydrogen
ERH2’s purpose is to create an energy demonstrator to generate and store hydrogen.
Notes: Dylan – our purpose is… in order to create facilities to take advantage of the DOE funding FUEL CELL

## Slide 8: System Requirements
Produce Hydrogen
1.1.1 The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.
Store Hydrogen
1.2 The storage method must run the fuel cell for a minimum of 5 minutes.
1.2.1 The system must measure the amount of hydrogen stored.
Run Fuel Cell
1.4 The system must interface with the Embry-Riddle fuel cell.
1.4.1 The system output must be a ¼” PTFE tube.
1.1.2 The system must be able to determine the rate of hydrogen gas produced.
Notes: Hannah- In fulfilling our purpose we have created requirements.

## Slide 9: System Description
Notes: Tesla

## Slide 10: ERH2 System Overview
Pressure Gauge
Electrolyzer
Storage & Extraction
Valves
Fuel Cell
Thermocouples
Stainless Steel Pipe
Notes: Tesla

## Slide 11: ERH2 System Overview
Notes: Tesla

## Slide 12: Electrolyzer Exploded View
Rubber Gasket
Polycarbonate Spacer
Copper Bus
Nickle Mesh
Notes: Grant
More explanation
Describe polycarbonate layers

## Slide 13: System Interfaces – Tee Fittings
¼ OD Compression Tee to ¼ NPT
¼ NPT Female to ¼ NPT Female
Pressure Gauge
J-Type Thermocouple
Notes: Titan
Show where we are getting it from

## Slide 14: System Interfaces – Valve Assembly
Barbed Fitting
¼ to ¾ NPT Reducer
¾ NPT Brass Ball Valve
¾ NPT to AN Flare Adaptor
Notes: Titan
Show where we are getting it from

## Slide 15: System Interfaces – Pipe Assembly
¾ AN Flare Sleeve
¾ Steel AN Flare Washer
¾ AN Flare Nut
¾ NPT to AN Flare Adaptor
Notes: Titan
Show where we are getting it from

## Slide 16: System Interfaces – Pipe Assembly
¾ AN Flare Sleeve
¾ Steel AN Flare Washer
¾ AN Flare Nut
¾ NPT to AN Flare Adaptor
Notes: Titan
Show where we are getting it from

## Slide 17: Material Storage
1 Micron Mesh
Hollow Stainless-Steel Capsule
Lithium-Doped Graphitic Carbon Nitride
Notes: Hannah- Inserted into the pipe is the material storage capsule. This capsule is a hollow steel tube with a 1 micron mesh on the ends to allow hydrogen to flow but not allow water into the material. The storage material we used is LiCN.

## Slide 18: Lithium-Doped Graphitic Carbon Nitride []
300°C will break the bonds to allow the hydrogen to escape.
Nitrogen Covalent Bonds
Graphitic Carbon Nitride
(Molecular Level)
Lithium Atoms
Hydrogen Molecules
Notes: Hannah
This is because the porous structures allow the hydrogen into interior of the nanotubes and pore edges containing double bonded nitrogen provide the active sites for adsorption of hydrogen either physically or chemically.

## Slide 19: Extraction Zone
Nichrome Wire Lead
Thermal Insulation
Electrical Insulation
Notes: Tesla

## Slide 20: Fuel Cell Integration
Requirement 1.4
“The system must interface with the Embry-Riddle fuel cell.”
Requirement 1.4.1
“The system output must be a ¼” PTFE tube.”
¼” PTFE
Fuel Cell
Notes: Titan

## Slide 21: Budget
Chart: 
| Electrolysis | Material Storage | Extraction | Interfaces | Piping | Instrumentation
 | 317.15 | 473.11 | 58.72 | 229.43 | 39.23 | 103.4
Total: $1221.04
$78.96 under budget
Notes: Dylan

## Slide 22: Budget
Total: $1495.07
$195.07 over budget
Chart: 
| Electrolysis | Material Storage | Extraction | Interfaces | Piping | Instrumentation
 | 367.15 | 545.11 | 99.72 | 269.43 | 54.23 | 159.43
Notes: Dylan

## Slide 23: Concept of Operations
Weigh material storage capsule
Turn on electrolysis and flush pipe until light turns on
Close exit valve to begin loading material storage
Run electrolysis until pressure gauge reads maximum pressure
Attach valve assembly onto pipe
Load capsule into pipe with rod
Notes: Dylan

## Slide 24: Concept of Operations
Once at 300°C, slowly open exit valve to power fuel cell
Reinsert capsule into pipe using loading rod
Turn on electrolysis and flush pipe until light turns on
Let fuel cell light turn off, close both valves and turn on heating element
Turn off electrolysis, disconnect pipe from valve, remove and weigh the capsule
Notes: Dylan

## Slide 25: Concept of Operations
Notes: Dylan

## Slide 26: Concept of Operations
Step 3: Reattach interfaces, ensure all valves are open.
Step 4: Turn on the electrolyzer and run until the fuel cell light turns on.
Notes: Dylan

## Slide 27: Concept of Operations
Notes: Dylan

## Slide 28
Closed Valve

## Slide 29: Concept of Operations
Step 7: Turn off electrolyzer, disconnect pipe from valve, remove capsule, and weigh again.
Notes: Dylan

## Slide 30: Concept of Operations
Step 8: Reload capsule into pipe.
Step 9: Run another flush.
Notes: Grant

## Slide 31: Concept of Operations
Step 10: Close both valves and turn on the heating element.
Notes: Grant
Mention heat to 300C

## Slide 32: Concept of Operations
Step 11: Once the capsule reaches 300°C, slowly open the valve to the fuel cell. Start a timer to measure how long the fuel cell light stays on.
Notes: Grant

## Slide 33: Verification Tests
Notes: GRant

## Slide 34: Production Rate
Requirement 1.1.1
“The system must produce enough hydrogen to get the fuel cell to steady state and then run for 10 minutes at 1 watt.”
Notes: Grant

## Slide 35
0.5x

## Slide 36: Material Storage
Starting Mass:
Ending Mass:
Ran the electrolyzer for 30 minutes.
of hydrogen stored
Notes: Hannah

## Slide 37: Material Capacity
Requirement 4.4
“The storage material must have a minimum hydrogen density of 2 wt%.”
Mass of Stored Hydrogen: 0.020 (g)
Mass of Material Total: 0.517 (g)
TEST INCOMPLETE
Notes: Hannah
Estimated amount of hydrogen needed

## Slide 38: Material Storage Benefits
 | Compressed Storage | Material Storage
Energy Density | 592.9-3796 J/m | 140-280 J/m^3
Weight Percentage | 3.53% | 3.87%
Storage Pressure | 60-500 bar | 1 bar
Notes: Hannah

## Slide 39: System Heating
Requirement 4.1
“The storage material must be heated to 300°C and not exceed 350°C.”
Applied Power
TEST INCOMPLETE
Max Temperature (200°C)
300°C Minimum
Power: 16.77W
350°C Minimum
Power: 23.56W
Notes: Tesla

## Slide 40: Thermal Survivability
Aluminum Silicate Fiber
Resistant to 815 °C
Silica Sleeve
Resistant to 1260 °C
Requirement 5.2
“The system must withstand temperatures up to 350°C.”
Nichrome Wire Lead
Notes: Tesla

## Slide 41: Pipe Heat Transfer
350°C
50°C
50°C
6 in
6 in
Worst-case scenario analysis:
Room Temperature (20°C)
350°C
Worst-case scenario testing:
Requirement 5.3
“The temperature at the valves must not exceed 50°C.”
Notes: Jacob Wolf

## Slide 42
Notes: Dylan

## Slide 43: Limiting Factors
Notes: Jacob

## Slide 44
“Murphy always gets a vote.”
- Dr. Michael Fabian
Notes: Jacob

## Slide 45: Blown-up Material Storage Capsule
Notes: Tesla

## Slide 46: New Material Storage Capsule
Notes: Tesla

## Slide 47: Cracked Electrolyzer
Greatest chemical attack occurs at stress concentrations.
Notes: Jacob

## Slide 48: New Electrolyzer End Panels
Notes: Jacob

## Slide 49: Future Recommendations
Notes: Jacob

## Slide 50: Improve Heat Transfer to Capsule
Notes: Hannah

## Slide 51: Shorten Pipe
Cut & Reflare
Notes: Jacob

## Slide 52: Prevent Hydrogen Leakage
Potential Problem Spots
Notes: Titan

## Slide 53: Future Tests
Release Tests
Capacity Tests
To be performed next Monday
Notes: Hannah

## Slide 54: Questions?

## Slide 55: References
[1] A. Murali, M. Sakar, S. Priya, R. J. Bensingh, and M. A. Kader, “Graphitic-Carbon Nitride for Hydrogen Storage,” in Nanoscale Graphitic Carbon Nitride, Elsevier, 2022, pp. 487–514. doi: 10.1016/B978-0-12-823034-3.00017-0.
[2] “Fast leakage test,” Unitem Wrocław, 28-Apr-2022. [Online]. Available: https://unitemmachines.com/our-offer/fast-leakage-test/. [Accessed: 08-Dec-2022].
[3] “Remington Industries.” [Online]. Available: https://www.remingtonindustries.com/
[4] “McMaster-Carr.” [Online]. Available: https://www.mcmaster.com/
[5] https://www.scielo.br/j/qn/a/KyQvF9DMHK6ZJXyL5zQNy7N/?lang=en&format=pdf
[6] https://www.gichemicals.ie/Potassium-hydroxide.html#:~:text=Potassium%20Hydroxide%20is%20manufactured%20using,concentrated%20to%2050%25%20using%20evaporation.
[7]“Aluminum silicate fiber felt and board,” Aluminum Silicate Fiber Felt and Board. [Online]. Available: https://www.samaterials.com/ceramic-material/2515-aluminum-silicate-fiber-felt-and-board.html. [Accessed: 21-Feb-2023].
[8] Heat Transfer Textbook

## Slide 56: Additional Slides
Requirements
Generation
  Natural Gas
  Photobiological
  Microbial Biomass conversion
Storage
  Physical
  Material
Equations
Graphic Design
Schedule
Ideal Gas

## Slide 57: Generation - Natural Gas
Methane Resource
Methane is collected from a source (usually from natural gas)
Steam-Methane Reforming
High temperature steam (at 700-1,000 °C) is added to the methane gas
Hydrogen Extraction
Hydrogen gas is extracted from the steam-methane mix from an added catalyst
Notes: The common catalyst used for steam-methane is typically nickel but research has been done showing that the noble metals can also work. This process produces hydrogen gas, carbon monoxide, and a small amount of carbon dioxide. DOE did not specify how much CO2 was produced.

## Slide 58: Generation - Photobiological
Bacteria Strain
Water is Supplied
Bacteria Uses Photosynthesis
Water is Broken Down into its Elemental Form
Hydrogen Gas is Released
Notes: After a complete cycle, the bacteria will need some amount of filtration provided, before adding more water. This filtration will remove all nitrates and acidic biproduct chemicals that was produced during a full cycle. During this process the bacteria will consume a percentage of the hydrogen gas, making the gas production rates and net efficiency of the system low.

## Slide 59: Generation - Microbial Biomass Conversion
Bacteria Strain
Hydrocarbon is Added
Bacteria Uses Fermentation
After Fermentation, the Bacteria Leaves Behind Several Elements
Hydrogen Gas can be Filtered Out.

## Slide 60: Storage – Physical Storage
Compressed
5,000-10,000 PSI
Unique Pressure Vessels
Cryogenic
Liquid H2 at -252.2 °C
Solid H2 at -259.14°C

## Slide 61: Storage – Material Storage
Adsorbtion
Hydrogen is Stuck to the Compound’s Surface
Absorption
Hydrogen is Encased by the Compound

## Slide 62: Equations – Area of Mesh

## Slide 63: Equations – Max Current

## Slide 64: Equations – Rate of O2 Production

## Slide 65: Schedule of Project
Date tracking Gantt ERH2 (version 1).xlsb.xlsx

## Slide 66: Ideal Gas Law
Where:
= Absolute pressure of the gas (KPa)
= Volume of the gas (L)
= Amount of the gas (g)
= Ideal gas constant (KJ/Kg*K)
= Absolute temperature of the gas (K)
Calculations

## Slide 67: Heat Loss / Required Power

## Slide 68: Vessel Pressure
Maximum Vessel Pressure: 40.43psia
  Champagne Bottle: 90psia
  Soda Can: 30psia

## Slide 69: Electrolysis Power Circuit
R1 = R3
Nickel Mesh
R2
Salt Water
Notes: Grant
Grant 1.25 in by resistance of saltwater 2 ohms per meter

## Slide 70: Risk Matrix – Before Mitigation
Notes: Hannah

## Slide 71: Pressure Requirement
Hard Copper Pipe
0.5”OD x 0.05”Wall Thickness x 2.63” Long
Requirement 10.2
“-”
PTFE Tubing
0.31”OD x 0.03” Wall Thickness x 2’ Long
Atmospheric Pressure: 14.7psi absolute
Maximum Internal Pressure: 14.7 + 0.29 = 14.99psi absolute
[3]

## Slide 72: Detecting Leaks
ERH2 will follow ASHRAE Bubble Method under Chapter 29.9 Leak Detection in the 2017 edition ASHRAE Handbook.
[2]